Description

The component in which flow is determined by state (and their derivatives) of connectors．
This behaves as “resistance” in system.
flow = f (state_a, state_b)

Flow: force
state: position of mass point.

Flow: force
(*into: positive)

Flow: force
(*into: positive)

state: position
state: position
Direction of positive position

Flow: heat flow (optional)
 = lossPower
 (*into: positive)

Governing equations
s_rel= flange_b.s - flange_a.s newline v_rel= dot s_rel newline f_c= c*(s_rel - s_rel0) newline f_d = d*v_rel newline f= f_c + f_d

lossPower= f_d*v_rel

Memo:
計算式のmmlファイルへの保存：計算式ボックスを左クリックで選択　→　右クリック　→　「名前を付けてコピーを保存」　→　「MathML 2.0」を選択